## Slide 1: Pluggable Optics Are Alive and Well
Toronto Wireline Workshop
Mike Bichan
Director, Analog Design, Marvell Optical PHY Group
March 6th, 2026

## Slide 2: My Background
FinFET
Backside Power
10G, 25G, 32G
NRZ
58G
DFE
Optical
224G,448G
128G
ADC
Source: OFC 2025

## Slide 3: What’s inside an optical module?
Egress
Ingress
Advantages:
hot-swappable
easier test
good thermals
faster design cycle
Drawback:
long channel from module to host

## Slide 4: Scaling Terminology
Scale-Up
Scale-Out
Scale-Across
Increase the capability of a single server
<1m
Density and latency are key
Active optical cable (AOC)
Co-Packaged Optics (CPO)
Short-reach PAM4 direct-detect
Add more servers within the same data centre
1m-1km
Long-reach PAM4 direct-detect
Power/perf trade-off
Interconnect multiple data centres
1km-1000km
Performance and spectral efficiency are key
Coherent transceiver
Wavelength-division multiplexing

## Slide 5: Optical Links
visible light is 380-750nm
850nm is produced by VCSELs
O-band (original), very low chromatic dispersion, used for datacom
C-band (conventional), lowest attenuation, used for coherent
Other bands (E-band, S-band, L-band, U-band) are less used
Source: Enrico Temporiti, “VCSEL-based Solutions: Components, Circuits and Integration”, ISSCC Short Course, 2026.

## Slide 6: Optical Links
Multi-mode fiber (MMF)
  50um core couples well to VCSEL emission pattern
  high loss: 2.5dB/km
Single-mode fiber (SMF)
  9um core
  low loss: 0.2-0.35dB/km
Source: Enrico Temporiti, “VCSEL-based Solutions: Components, Circuits and Integration”, ISSCC Short Course, 2026.

## Slide 7: Optical Links
Intensity Modulation and Direct-Detection (IMDD)
  Only uses light intensity, not phase
  Lower power and performance
Coherent
  Sensitive to the intensity, phase, and polarization of light
  Polarization diversity receiver corrects for many non-idealities
  Requires a single laser source and single clock source
  High power and performance
  Used with dense wavelength division multiplexing (DWDM)
(a) Direct-Detect Transmitter
(a) Coherent Transmitter

## Slide 8: Optical Links
VCSEL diode driven directly by transmitter
Conventional Mach-Zehnder modulator (MZM)
  Electric field directly changes refractive index (Pockels effect)
  : voltage required for 180° phase shift, times length
  LiNbO3, TFLN, InP
Silicon photonic MZM
  Leverages CMOS infrastructure
  Silicon has no Pockels effect
  Place a reverse-biased PN junction inside the waveguide, allows applied electric field to deplete charge carriers which indirectly affects refractive index
Electro-absorption modulator (EAM)
  InGaAsP-on-InP
  Franz-Keldysh or quantum-confined Stark effect
  Applied electric field changes absorption of photons
  Integrated with DFB laser in an electro-absorption modulated laser (EML)
  Commonly single-ended

## Slide 9: High-Swing CMOS Transmit Driver
Source: V. Gurumoorthy et al., “A 212Gb/s PAM-4 Retimer with Integrated High-Swing Optical Driver and Chip-to-Module Long Reach Capability of 40dB in 5nm FinFET”, ISSCC, pp. 344-345, Feb. 2025.

## Slide 10: TDECQ
TDECQ: Transmitter and Dispersion Eye Closure Quaternary
It measures how much more optical power is needed for a real transmitter to achieve the same error rate as an ideal transmitter
Steps:
  Transmitter sends SSPRQ pattern
  Optical signal goes through 1m fiber then photodiode
  4th-order Bessel filter with bandwidth at Nyquist
  Optimize receive equalizer tap values (5-, 9-, or 15-tap)
  Measured histograms around the received eye center
  Determine added noise required to reach target error rate
Source: 802.3bs Ethernet spec
TDECQ < 3.4dB

## Slide 11: Optical Links
Can save power by pushing retiming to switch ASIC
Reduces performance
More complicated link budget

## Slide 12: Optical Links
Overwhelming majority of optical links are currently using pluggable optics
Moving optics closer to switch ASIC:
  Saves power
  Reduces latency
  Overcomes high loss from host to module
Co-Packaging Challenges:
  Optics don’t benefit from proximity to switch ASIC
  Lower power budget for optics
  Test is more difficult
  Not hot-swappable, upgradeable
  Switch ASIC is hot
  High temperature degrades:
    laser slope efficiency, TIA noise, modulator Vpi, jitter, electromigration

## Slide 13: Optical Links
Low-cost DSP with integrated TIA
Attractive for pre-built cable market

## Slide 14: Optical Links
DSP
  CMOS
TIA
  SiGe, InP
PD
  III-V, Ge-on-Si
Modulator
  LiNbO3, InP, Si

## Slide 15: Optical Links
High Data Rate Challenges:
BW + ESD protection
Tight jitter spec
Hard power budget
Baud Rate [Gbaud] | Chip-to-Module Loss [dB]
25 | 10
50 | 22
100 | 37
200 | ?

## Slide 16: >400Gbps/lane Direct-Detect at OFC 2025
2 demos with external partners
Joint Marvell demos with Lumentum and Terahop
Optical TX
Lumentum 225GBaud
Terahop (Innolight) 215GBaud
Source: OFC 2025