## Slide 1: Future of I/O: optical vs Electrical + Optical
Masum Hossain

## Slide 2: The boundary between Electrical and Optical Links
UCIe (advanced)
UCIe (standard)

## Slide 3: Outline
Evolution of Optical Links towards lower power
Silicon Photonics
  Monolithic vs Co-Packaged
  Approach 1: Wide Parallel Interface
  Approach 2: Optimizing bandwidth/λ
Electrical Alternative: Co-packaged Copper
What about On Package Photonics?
What about On Die photonics?
Summary

## Slide 4: Pluggable Optics – need to improve energy efficiency

## Slide 5: Pluggable Optics – need to improve energy efficiency

## Slide 6: Simplify ASIC to Module connectivity
Bringing optics closer to the ASIC we can reduce the ASIC to EIC loss to XSR
Further power reduction can happen if CMOS can directly drive the modulator and eliminate the off-chip TIA if SNR allows.

## Slide 7: Example: Broadcom’s Tomahawk

## Slide 8: Why Co-Packaged Optics?
Pluggable Optics: 15 pJ/bit
Near Package Optics (NPO)/LPO:
XSR Link 2 pJ/bit
Optical Transceiver: 5 to 7 pJ/bit
Bandwidth: 64x100 Gb/s
Co-Packaged Optics:
Die-to-Die : 0.3 pJ/bit
Optical Transceiver: 5pJ/bit
Latency < 50 nsec
Bandwidth > 1 Tb/s

## Slide 9: CPO options: Monolithic vs Co-Packaged
GF 45nm SPCLO Process

## Slide 10: Slow and Wide Monolithic Approach

## Slide 11: Slow and Wide Monolithic Approach
[Wade OFC’2018]

## Slide 12: NVIDIA CPO: 32 Gb/s Links in 7nm FinFET EIC

## Slide 13: NVIDIA CPO: 32 Gb/s Links in 7nm FinFET EIC

## Slide 14: Summary of NRZ DWDM Links
DWDM per-λ data rate is relatively low compared to CWDM
  Can utilize wide and parallel D2D interface (UCIe, AIB, BoW, OpenHBI, etc)
    No need power-hungry SerDes
    Preserve low power and low latency
 |  | IMEC ISSCC 2015 | Intel VLSI 2022 | AMD ISSCC 2023 | Intel VLSI 2023 | Ayar Labs VLSI 2024
 |  | TRX | TRX | RX | RX | TRX
Process | EIC | 40nm | 45nm SOI | 7nm | 28nm | 45nm SOI
 | PIC | 130nm SOI |  | 45nm SOI | Intel SiPh | 
# of wavelengths |  | 4 | 8 | 7 | 8 | 8
Per-λ Data Rate (Gbps) |  | 20 | 16 | 50 | 32 | 32
Per-Fiber Data Rate (Gbps) |  | 80 | 128 | 350 | 256 | 256
Modulation |  | NRZ | NRZ | NRZ | NRZ | NRZ
RX Sensitivity OMA (dBm) @ 1e-12 |  | -7.2 | N/A | -10.1 | -10 | -14.2
Energy Efficiency (pJ/b) |  | 2.33 | 5 | 0.96 (RX only) | 3.8 (RX only) | 3.45
NVIDIA 2026
TRX
7nm finFET+
65nm PIC
9
32
256
NRZ
-16
2.59 (RX only)

## Slide 15: Slow and Wide Silicon Photonics Solution
Energy Efficiency: 0.3 pJ/bit + 3 to 4 pJ/bit + 0.3 pJ/bit
Latency 3 ns 10 ns 3ns
Bandwidth : 8x32 Gb/s = 256 Gb/s
Bandwidth Density : ~0.5 to 1 Tb/s/mm
Cost: High
Additional Challenges: Thermal stability, volume manufacturability

## Slide 16: Packaging of 3D SiPh Transceiver
TSVs in PIC
Embedded silicon bridge to support fine-pitch D2D I/O
FAU integration w/ PIC grating couplers
Power delivery through LGA, substrate DSC and LSC
Optical I/O Chiplet in XPU Package
XPU
Organic Substrate
Silicon Bridge
Cold Plate
Organic interposer

## Slide 17: Improving Bandwidth and Thermal Stability
EIC flip-chip-attached to PIC through Cu pillars
32 Gb/s/λ  56 Gb/s/λ (NRZ)  112 Gb/s /λ
EAM Modulators in proximity to XPU
8λ based WDM using Ring Modulator

## Slide 18: Transmitter and Driver
OMA = -4.4 dBm
Measurement Setup
56 Gbps OTX Eye
TX Signal Path
Ref. [16]

## Slide 19: SNR Optimized Receiver

## Slide 20: Photonic Fabric Test Vehicle
4 * 56 Gbps/ = 224 Gbps/fiber
16 transceiver lanes, 1.8Tbps bisectional BW in <2mm2
5nm CMOS EIC
4 channels, 4 lanes per channel

## Slide 21: Measurements: WDM Mode, Power
~0.5 dB penalty due to WDM
Electronics: 2.8 pJ/bit
Laser: ~1 pJ/bit
Chart: 
| TX clocking | Serializer | Pre-driver | EAM driver | TIA | Sampler | RX clocking | Deserializer | PLL & Bias
 | 19 | 10.1 | 7.3 | 12.6 | 19.3 | 27.5 | 43.7 | 3.5 | 13

## Slide 22: Summary of NRZ DWDM Links
DWDM per-λ data rate is relatively low compared to CWDM
  Can utilize wide and parallel D2D interface (UCIe, AIB, BoW, OpenHBI, etc)
    No need power-hungry SerDes
    Preserve low power and low latency
 |  | IMEC ISSCC 2015 | Intel VLSI 2022 | AMD ISSCC 2023 | Intel VLSI 2023 | Ayar Labs VLSI 2024
 |  | TRX | TRX | RX | RX | TRX
Process | EIC | 40nm | 45nm SOI | 7nm | 28nm | 45nm SOI
 | PIC | 130nm SOI |  | 45nm SOI | Intel SiPh | 
# of wavelengths |  | 4 | 8 | 7 | 8 | 8
Per-λ Data Rate (Gbps) |  | 20 | 16 | 50 | 32 | 32
Per-Fiber Data Rate (Gbps) |  | 80 | 128 | 350 | 256 | 256
Modulation |  | NRZ | NRZ | NRZ | NRZ | NRZ
RX Sensitivity OMA (dBm) @ 1e-12 |  | -7.2 | N/A | -10.1 | -10 | -14.2
Energy Efficiency (pJ/b) |  | 2.33 | 5 | 0.96 (RX only) | 3.8 (RX only) | 3.45
NVIDIA 2026
TRX
7nm finFET+
65nm PIC
9
32
256
NRZ
-16
2.59 (RX only)
Celestial 2025
TRX
5nm finFET+
PIC
4
56
256
NRZ
-11
2.8 (RX only)

## Slide 23
Scaling Options for CPO
Multi-Row FAU enhances the escaped beachfront density from OE.
https://tspasemiconductor.substack.com/p/from-chips-to-optics-tsmcs-metalens
Notes: As shown by the right-hand side of this slide, the beachfront density, the y-axis, is dictated by how many rows of fibers we have on a fiber array units, or FAU, the x-axis and how fast we pass data on each fiber, the colors of lines.
Vertical-light-paths of grating couplers, rather than in-plane paths of edge coupling, allow multi-row FAU. This significantly increases the number of optical connections and, consequently, the beachfront density attainable.
However, as shown in the left side of the slide, this approach has challenges related to mechanical alignment of fibers, and focusing issues of the silicon lenses. This is because it needs a mirror or prism to make a 90-degree turn.

## Slide 24: Electrical Alternative: Co-Packaged Copper
Bandwidth density
4*64*224/80 ~ 700 Gb/s/mm
4*64*448/80 ~ 1.4 Tb/s/mm

## Slide 26: XPU to XPU/Switch Connectivity Options
Energy Efficiency: 0.3 pJ/bit + 3 to 4 pJ/bit + 0.3 pJ/bit
Latency 3 ns 10 ns 3ns
Bandwidth : 8x32 Gb/s = 256 Gb/s
Bandwidth Density : ~0.5 to 1 Tb/s/mm
Cost: High
Additional Challenges: Thermal stability, volume manufacturability
Reach 50 meters
Energy Efficiency: 0.3 pJ/bit + 5 to 7 pJ/bit + 0.3 pJ/bit
Latency 3 ns 100 ns 3ns
Bandwidth : 4x64x 224 Gb/s
Bandwidth Density : 0.7 to 1.4 Tb/smm
Cost: Low
Reach\: 1 m to 2 m

## Slide 27: Extending Electrical Link Speed
Unlike Optical, the degree of freedom is very limited.
Channel and connectors have to improve
MLSD or other Advanced signal
processing is a must [ Hossain Shakiba’23 IEEE 802..]
Combine MLSE with FEC to get
More coding gain [ Prof. Carusone
Group Design Con]

## Slide 28: Bandwidth Density Enhancement with Micro-LED Array
Avicena Tech

## Slide 29: Micro-LED Array-Based Slow and Wide

## Slide 30: Photonic Die to Die with longer reach
SNR and bandwidth limitations must be addressed through innovative modulation
Reach: up to 10 meters
Micro-LED bump mitch can be 15 to 20 um
Possible Bandwidth Density:
60 x 60 x 5Gb/s  18 Tb/s/mm^2
Can we do it with 2 pJ/bit?
MIMO
Encoder
Driver
Array

## Slide 31: Optics inside the IC

## Slide 32: Optics inside the IC

## Slide 33: Summary
Next 2 to 3 years: Co-Packaged Copper will be used for cost and maturity
  Need better FEC and MLSD
  SNR is the main challenge
Next 3 to 6 years: Co-Packaged Optics will show up in products
  Maturity and Cost
  Comb laser source
  Coherent will take more solution space compared to IMDD
Next 8 to 10 years: Micro-LED-based links will find some solution space
  SNR challenge
  Bandwidth Challenge
Die-to-Die: will remain electrical for the highest escape bandwidth
10+ Tb/s/mm